## Slide 1: Elisa
R.Sowmya
Assistant Professor
St peter’s Institute Of Pharmaceutical sciences

## Slide 2
Enzyme-Linked Immunosorbent Assay (ELISA) is a modern molecular method
used to detect interactions between antigens and antibodies through the use of
enzymes.
It stands as one of the most sensitive enzyme immunoassays available for identifying and quantifying the presence of antigens or antibodies, particularly in clinical diagnostics for a range of diseases.
The antigens or antibodies are tagged with enzymes like alkaline phosphatase, horseradish peroxidase, and β-galactosidase.
A chromogenic substrate specific to the enzyme (Ex: o-phenyldiamine dihydrochloride for peroxidase or p-nitrophenyl phosphate for alkaline phosphatase) is added.
The enzyme bound to the antigen-antibody complex acts on the substrate—usually hydrolyzing it—to produce a color change.

## Slide 3
This color change can be observed visually or measured by reading the optical density with a microassay plate reader (commonly referred to as an ELISA reader). A standard curve, established using known concentrations of antigen or antibody, is typically prepared to calculate the unknown quantities.
ELISA techniques can be broadly divided into four categories:
Direct Elisa
Indirect Elisa
Sandwich Elisa
Competetive Elisa

## Slide 4
Direct ELISA
It is the simplest and fastest approach, using a single enzyme-linked antibody that
binds directly to the antigen in the sample.
Procedure:
Antigens coated on to the wells of a microtiter plate, where the antigen adsorbs to the surface.
Wash to remove any unbound antigen.
Introduce an enzyme-conjugated antibody that attaches to the bound antigen.
wash to eliminate excess unbound antibodies.
Add a chromogenic substrate, which reacts with the enzyme to produce a color change that is used for interpretation.

## Slide 5
Indirect ELISA
It uses a secondary enzyme-linked antibody to detect the primary antibody bound to the antigen.
Procedure:
Immobilize known antigens that are specific to the antibody of interest in the wells.
Carefully wash the wells to remove any unbound or contaminant antigens.
Add the serum sample; if specific antibodies are present, they will bind to the immobilized antigen.
Wash again, then add an enzyme-linked secondary antibody that targets the bound primary antibody.
After another wash, add a substrate to observe the resulting color change.

## Slide 6
Sandwich ELISA
This is mainly used for antigen detection.
Procedure:
Coat the well with capture antibodies.
Wash to remove any unbound capture antibody.
Add the sample containing the antigen, allowing it to bind to the capture antibodies.
Wash again, then add the enzyme-linked detection antibody, which binds to a different site on the antigen.
After a final wash, add the substrate and the color change indicates the presence of the antigen.

## Slide 7
Competitive ELISA
Procedure:
Primary antibody (unlabeled) is incubated with sample antigen.
Antibody-antigen complexes are then added to well plates which are pre-coated with the same antigen.
Unbound antibody is removed by washing the plate. (The more antigen in the sample, the less antibody will be able to bind to the antigen in the well, hence “competition.”)
The secondary antibody that is specific to the primary antibody and conjugated with an enzyme is added.
A substrate is added, and the remaining enzymes elicit a chromogenic or fluorescent signal.

## Slide 8
THANK YOU